OPERATION MANUAL

NUAGE™

MULTI-PURPOSE ALL ELECTRIC

LIFT TABLE

FOR COMMERCIAL USE ONLY

(800) 358-8292     (760) 597-2155

Fax: (760) 599-7374

# OPERATION MANUAL

# Living Earth Crafts

Nuage All Electric Lift Table

Your new Living Earth Crafts Nuage Lift table is an electronically operated table. This manual will assist you in operating and caring for your new table.

Section 1:	IMPORTANT SAFETY INSTRUCTIONS	page 2-4

.

Section 2:	OPERATING INSTRUCTIONS	page 5-6

Section 3:	MAINTENANCE	page 7-8

Section 4:	TROUBLE SHOOTING 	page 9

Section 5:	TECHNICAL PROBLEMS	page 10

Section 6:	WARRANTY	page 11

Section 7:   SPECIFICATIONS	page 12

Section 1

NUAGE TABLE

IMPORTANT SAFETY INSTRUCTIONS

FOR COMMERCIAL USE ONLY

When using an electrical furnishing, basic precautions should always be followed, including the following:

Read all instructions before using the NUAGE TABLE.

DANGER- To reduce the risk of electrical shock:

- Always unplug this furnishing from the electrical outlet before cleaning.

WARNING- To reduce the risk of burns, fire, electric shock, or injury to persons:

- Unplug from outlet before putting on or taking off parts.

- Close supervision is necessary when this furnishing is used by, or near children, invalids, or disabled persons.

- Use this furnishing only for its intended use as described in these instructions. Do not use attachments not recommended by the manufacturer.

- Never use this furnishing if it has a damaged cord or plug, if it is not working properly, if it has been dropped or damaged, or dropped into water. Return the furnishing to a service center for examination and repair.

- Keep the cord away from heated surfaces.

- Never operate the furnishing with the air openings blocked. Keep the air openings free of lint, hair and the like.

- Never drop or insert any object into any opening.

- Do not use outdoors.

- Do not operate where aerosol (spray) products are being used or where oxygen is being administered.

- To disconnect, turn all controls to the off position, then remove plug from outlet.

- WARNING, MOVABLE PARTS- Risk of Injury- Keep children away from extended Table Lift, Back Support or Leg Support.

- CAUTION: To reduce the risk of electrical shock, this furnishing has a grounded plug. If it does not fit, contact a qualified electrician to install the proper outlet. Do not change the plug in any way. See page 4.

- Make certain that the cord and plug are maintained in good condition and are not allowed to become damaged while in use. Avoid positioning the cord in the traffic lane and it is always kept out of the way. Take this furnishing out of service immediately if the cord or plug becomes damaged in any way.

- If this furnishing is not in use, the cord needs to be rolled up and stored out of the way to avoid damage.

- Do not attempt to repair this furnishing. All repairs must be performed by an authorized service representative.

SAVE THESE INSTRUCTIONS

Section 1, Continued

## IMPORTANT SAFETY INSTRUCTIONS

Nuage Electric Lift

CAUTION!

When lowering any section of the table, make sure that no supplies or any part of yours or your client’s body is between the top of your table and its base.  This could result in injury, or could damage your table as well as the item.   It is recommended that you always return your table top to the lowest flat position to avoid leaving the base exposed.  By doing so, you will minimize the possibility of damage to your table by unequal weight distribution such as sitting on the leg section while raised.

When lowering the table height, be sure there are no foreign obstacles underneath your table that could obstruct it from lowering completely. This could damage your table.

- Maximum weight lifting capacity of 550 lbs, maximum load limit for the back and leg section 100 lbs each.

- Never set anything under the table frame.

- Never operate your table on an uneven surface.  Adjust the leveling feet so that your table is stable.

- Never operate your table with unequally distributed weight such as sitting on the foot or head section while raising or lowering it.

- Never raise the head or foot section with a client in the prone position (face down).

- Never use or store your table in a wet or very humid environment. Water and excessive moisture can damage the wood cabinet and electrical components. Evidence of exposure to water or moisture will void your warranty.

- If you have purchased the Flexible Armrest Option, never use the Armrests as handholds or body support mechanisms, especially when setting clients on or off the table.

- Never attempt to use the foot lift section to support concentrated weight such as sitting or standing.

SAVE THESE INSTRUCTIONS

Section 1, Continued

## IMPORTANT SAFETY INSTRUCTIONS

Nuage Electric Lift

GROUNDING INSTRUCTIONS

This product must be grounded. If it should malfunction or breakdown, grounding provides a path of least resistance for electric current to reduce the risk of electric shock. This product is equipped with a cord having an equipment-grounding conductor and grounding plug. The plug must be plugged into an appropriate outlet that is properly installed and grounded in accordance with all local codes and ordinances.

DANGER- Improper connection of the equipment-grounding conductor can result in a risk of electric shock. Check with a qualified electrician or serviceman if you are in doubt as to whether the product is properly grounded. Do not modify the plug provided with the product-if it will not fit the outlet, have a proper outlet installed by a qualified electrician.

This product is for use on a nominal 120-volt circuit and has a grounding plug that looks like the plug illustrated in sketch (A) below. Make sure that the product is connected to an outlet having the same configuration as the plug. No adapter should be used with this product.

SAVE THESE INSTRUCTIONS

# Section 2

## OPERATING YOUR TABLE

Nuage Electric Lift

The Arrows on the top row indicate “Up” or “Down”

and will articulate the section of the table that is darkened in the image

Use of Hand Control:

With your new Nuage table, you can

- Raise or lower the head section independently

BACK TILT ARTICULATES BY TOUCHING THE ICONS ON THE TOP ROW.

- Raise or lower the leg section independently

CALF SECTION ARTICULATES BY TOUCHING THE ICONS IN THE SECOND ROW

- Raise or lower the height adjustment

HEIGHT RANGE MOVES BY TOUCHING THE ICONS IN THE THIRD ROW

  - Preset Position 1: flat massage position

  - Preset Position 2: facial position

  - Preset Position 3: enter/exit table position

  - Preset Position 4: body treatments

Use of Foot Control:

The foot pedal controls the raising or lowering of the entire table. The left side raises the table and the right side lowers it.

# Section 2 - Continued

## OPERATING YOUR TABLE

Nuage Electric Lift

# Moving your Nuage Table.  To avoid damage to your Nuage table, it is very important that the table only be lifted at certain positions on the table.

# OPTION: Flex Armrest. Applies only to tables purchased with this option.

The optional flexible armrest on your Living Earth Crafts table features a positive lock design. A locking mechanism ensures that the armrests do not unexpectedly pull out during use. At first the armrests will be a bit tight to remove.  This is normal.  Allow time to let the components “fit in”, and they will loosen over time.

- Install the Flex Armrests. Installing the armrests can be done with the table in any position, however, it may be easiest when the table top is in the flat position. Line up the entry posts with the side grommet holes. Push the tips into the holes until a click can be heard. If the armrest is pushed in too far, pull it back slightly and the lock will engage. Test the locked position by giving it a light pull. It should give resistance.

- Remove the Flex Armrests. Removing the armrests can be done with the table in any position, however, it may be easiest when the table top is in the flat position. Grasp the armrest near the entry posts and remove one end at a time with a sharp pull. This operation takes some effort, however this ensures that the rest will not release during use.

Section 3

## MAINTENANCE

Nuage Electric Lift Table

Your new Nuage table is relatively maintenance free as the lifting mechanism is enclosed and sealed.  However, to ensure that your table will continue to function properly and keep its appearance, we recommend the following:

- VINYL: After each and every treatment on your table, clean thoroughly, removing all oil residue. This and other residues may cause the vinyl to dry out and become brittle.  We recommend using the product ViraGuard® (sold by Living Earth Crafts) which also disinfects.  Spray the vinyl and rub gently with a soft cloth.   A solution of 1 part mild detergent (such as liquid dishwashing detergent) to 10 parts warm water may also be used. Simple Green is another alternative. A more thorough cleaning is recommended on a weekly basis.

Use caution when attempting to remove stains as you could damage your vinyl. Any stains should be treated immediately with a solution of 1 part alcohol to 10 parts water. Restore the luster to the spot with a light application of spray furniture wax.

CAUTION!

DO NOT USE ACETONE, PAINT THINNER, BLEACH,

ARMOR ALL TYPE OR INDUSTRIAL CLEANERS.

These will damage the vinyl’s protective coating.

Section 3 - Continued

## MAINTENANCE

Nuage Electric Lift

- It is recommended that you periodically check the leveling feet to be sure the table is level and stable. This is especially important if the table has been moved.

The “level or balance” of your table is very important, both during the initial set up and on a routine basis. The balance of the table is adjusted with the leveling feet, located on the bottom of each leg. You will need (2) open end wrenches – ½” and 9/16”.

Begin by taking a visual inspection of the flat bottom foot of each leg. Notice two hex nuts on each leveling foot. The upper hex nut is adjustable and secures the leveling foot in place, while the lower nut is stationary, and allows you to raise and lower each leveling foot independent of each other. This is necessary as floors and carpet may not be 100% level or flat. The most common symptom of an unbalanced table is unusual rocking of the entire bed. To determine which foot to adjust, attempt to “rock” your table. If your table rocks, the leg that is “off the ground” is the one that will need adjusting. Once your diagnosis has been made, proceed as follows:

- Raise table height to approximately 6 inches off the floor.

- Loosen the upper hex nut until it no longer touches the upper leg.

- Raise or lower the entire foot as necessary on the lower hex nut. Counterclockwise will lower the overall height; clockwise will raise the overall height. Continue with the adjustment of the lower hex nut until the black round foot is completely flat to the ground and the table no longer rocks.

- To lock into place, reposition the upper hex nut so that is secure and tight against the upper leg.

- Test all legs to ensure that the upper hex nut is tight against the upper leg and secure in place.

3.   This furnishing has no user serviceable parts.

4.    If this furnishing is taken out of service, the electrical cord needs to be rolled up and placed inside the table to avoid damage while in storage.

#### Section 4

#### TROUBLE SHOOTING

Nuage Electric Lift

If you are experiencing technical difficulties with your Nuage table, we ask that you perform these trouble shooting techniques prior to contacting Living Earth Crafts.

SYMPTOM: Table does not raise or lower:

- Check to make sure the outlet in your room is receiving power. This can be done by plugging in a hairdryer or small appliance and turning it on.

- If you have a dimmer in the room, make sure the dimmer switch is turned to full power, then retest your table.

- Check the fuse or circuit breaker box for blown fuse or tripped circuit breaker.

SYMPTOM: Table is unstable after moving it to a new location:

- See Section 3: Maintenance regarding leveling your table.

If you are unable to resolve the problem with your table, please refer to Section 5, Technical Problems, and contact Living Earth Crafts.

#### Section 5

#### TECHNICAL PROBLEMS

Nuage Electric Lift

With proper maintenance, your Living Earth Crafts table is designed to give you years of trouble free operation.  If you should have a problem with your table, do not attempt to repair the table yourself.  This will void the 2-year warranty that covers your table against defects in material and workmanship. To maintain your warranty, you need to follow these steps:

- Call 800-358-8292 or 760-597-2155

Our Customer Service Representative will ask you to provide the following information:

- your table’s serial number (located on the underside of the head

section of the table top)

- a description of the problem

- Please remember that any unauthorized service will not be covered.  Please be sure to contact us first.

- As expressed in your warranty, damage from abuse or mishandling is not covered.

You will need to allow the technician access to your table at the scheduled time.  If there is a lengthy delay, you will be charged for the delay time at the service agent’s hourly rate.  To cancel the appointment, notify the technician 24 hours prior to the scheduled appointment.  If you fail to notify the technician, you will be charged for the service call.

#### Section 6

#### WARRANTY

Nuage Electric Lift

## Tables are warranted against defects in materials, design and workmanship, to the original owner, as follows:

## Frame

## Lifetime (

## Foam & Vinyl

## 3 years

## Motors, Controls, Electronics

## - 2 years

## Warranty is onsite where available.

## Warranty does not cover damage caused by accident, misuse, or neglect. All warranties limited to repair or replacement, at our discretion, to the original purchaser.

## ( Lifetime warranty applies to original owner, as long as you own your table or 5 years after the model is discontinued or five years for private label tables

## Section 7

NUGAGE ELECTRIC LIFT

## SPECIFICATIONS

FEATURES:

(Top Width options:  30” or 32”

(Length:  73”

4” Strata Memory Foam

( Height Range: 27” to 38”

(Electric Lift

(Heavy-Duty foot pedal to raise and lower table

(Power Supply:  110 volt, Standard Wall Outlet

(International Power Supply:  Alternate voltages and plugs available for all countries

(Lifting capacity:  550 lbs

(Standard Base: Cabinet

(Standard Top: Salon Top

( Electric lifting system

( ¾” Veneer Core Ply

( Solid hardwood Maple & ¾” Multi-ply frame construction

( Includes:

( Neck Roll

( Heavy Duty Foot & Hand Controls

( Electric Salon Top

( Round Corners

ELECTRICAL DATA –

ELECTRICAL INFORMATION

120VAC or 22-240VAC

4 Amp MAX draw (average draw is approx 3 Amp

50-60 Hz

Control Box for Foot Control

IN: 120vac - 60 Hz, IN: 600W, OUT: 18VDC

# Text boxes

Only lift your Nuage table in the areas circled. Do not lift from any section marked with an “X”.

Your bed can be lifted from the bottom of the table by grasping firmly onto the frame. Do not try to lift from the fins on the Cuvee or the doors on any Nuage table.

Your table can be lifted from the side at the point where the table top is attached to the frame. Do not lift the bed from any portion of the table top that is not securely attached to the frame.

CAUTION: Your Nuage table is very heavy and extreme caution should be used to avoid injury to yourself, others around you, and your Nuage table.

X

X

X

X