OPERATION MANUAL

NAPA LA MER™

MANUAL HYDRAULIC LIFT TABLE

For tables manufactured

January 2006 – Current

(800) 358-8292     (760) 597-2155

Fax: (760) 599-7374

# OPERATION MANUAL

# Living Earth Crafts

Napa La Mer Manual Hydraulic Lift

Your new Living Earth Crafts Napa La Mer Wet/Dry Treatment Table with Manual Hydraulic Lift table is a manually operated lift table. This operational manual will assist you in operating and caring for your new table.

Section 1:	IMPORTANT SAFETY INSTRUCTIONS	page 2

.

Section 2:	OPERATING INSTRUCTIONS	page 2

Section 3:	MAINTENANCE	page 3, 4, 5, 6

Section 4:	TECHNICAL SERVICE	page 7

Section 5:	WARRANTY	page 8

Section 6:	SPECIFICATIONS	page 9

Section 1

NAPA LA MER TABLE

IMPORTANT SAFETY INSTRUCTIONS

FOR COMMERCIAL USE ONLY

When using this hydraulic furnishing, basic precautions should always be followed, including the following:

Read all instructions before using the NAPA LA MER TABLE.

CAUTION!

When lowering the table height, be sure there are no foreign obstacles underneath your table. This could damage your table.

- Close supervision is necessary when this furnishing is used by, or near children, invalids, or disabled persons.

- Use this furnishing only for its intended use as described in these instructions. Do not use attachments not recommended by the manufacturer.

- If this product is not working properly, if it has been dropped or damaged, or dropped into water, return the furnishing to a service center for examination and repair.

- Never drop or insert any object into any opening.

- WARNING, MOVABLE PARTS- Risk of Injury- Keep children away from moving parts.

- Never exceed the maximum weight lifting capacity of 500 lbs.

SAVE THESE INSTRUCTIONS

# Section 2

## OPERATING YOUR TABLE

Height Adjustment: Your new Napa La Mer Manual Hydraulic Lift Table can be raised and lowered to adjust the working height by using the hand crank.  The hand crank folds away when not in use.

To raise or lower your table, flip out the hand crank by pulling the crank handle towards you, and flipping the handle up.  Turn the crank clockwise to raise the table.  Use a slow, steady turning motion.  Do not try to spin the crank or force it.  When the table reaches its maximum height, the pump will stop.  Use caution as, if force is applied, the pin connecting the crank handle to the pump could break.  When lowering the table, use the same slow, steady motion turning counterclockwise.  Do not try to force the table down by pushing on it.  When the desired height is reached, fold the hand crank away.  To fold the hand crank under the table, pull the handle towards you, then fold underneath the table top. Do not leave the hand crank in the cranking position while using the table.  The exposed hand crank could get broken or cause injury to yourself or your client.

Section 3

## MAINTENANCE

Your new Napa La Mer Manual Hydraulic Lift table is relatively maintenance free.  However, to ensure that your table will continue to function properly and keep its appearance, we recommend the following:

VINYL CLEANING

Advanced BeautyGard™ Protective Finish
Cleaning is a breeze with Aqua™ brand fabric and its Advanced BeautyGard protective finish. While staining and soiling exposures are common to upholstery fabrics, most stain and soiling may be removed by using the simple cleaning methods that follow:

For Light soiling:
1. A solution of 10% household liquid dish soap with warm water applied with a soft damp cloth will remove most soiling.

2. If necessary, a solution of liquid cleanser and water applied with a soft bristle brush. Wipe away the residue with a water-dampened cloth.

For Heavier soiling not solved by above method:
1. Dampen a soft white cloth with lighter fluid (naphtha) and rub gently. Rinse with a water-dampened cloth.

NOTE: Use extreme caution with this method. Complete only in a well-ventilated area and away from any open flame.

NOTE: You should try this method on an inconspicuous spot before using it on the original stain/soiling.

For the most difficult stains not removed by the above methods:
1. Dampen a soft white cloth with a solution of household bleach (sodium hypochlorite); 10% bleach, 90% water.

2. Rub gently. 

3. Rinse with a water-dampened cloth to remove bleach concentration.

4. If necessary, allow a 1:10 diluted bleach solution to puddle on the affected area or apply with a soaked cloth for approximately 30 minutes. Rinse with a water-dampened cloth to remove any remaining bleach concentration. 

NOTE: You should try this method on an inconspicuous spot before using it on the original stain/soiling.

MAINTENANCE

VINYL CLEANING – CONTINUED

Note
To restore luster, a light coat of spray furniture wax can be used. Apply for 30 seconds and follow with a light buffing using a clean white cloth.

Antimicrobial
Aqua vinyl with Advanced BeautyGard provides outstanding protection in difficult medical and health care environments.

Contains agents effective against bacterial and fungal microorganisms.

Please Review Carefully
CAUTION: Should you desire to use other cleaning methods, carefully try them in an inconspicuous area to determine potential damage to the material. Never use harsh solvents or cleaners which are intended for industrial applications. To clean stained or soiled areas, a soft white cloth is recommended. Avoid use of paper towels.

CAUTION: Cleaning products may be harmful/irritating to your skin, eyes, etc. Use protective gloves and eye protection. Do not inhale or swallow any cleaning product. Protect surrounding area/clothing from exposure. Use in a well ventilated area. Follow all product manufacturer’s warnings. Aqua cannot be held responsible for damage or injuries resulting from the use or misuse of cleaning products.

We recommend cleaning after each and every treatment on your table. Clean thoroughly, removing all oil residue. This and other residues may cause the vinyl to dry out and become brittle.

CAUTION!

DO NOT USE ACETONE, PAINT THINNER,

ARMOR ALL TYPE OR INDUSTRIAL CLEANERS.

These will damage the vinyl’s protective coating.

MAINTENANCE – CONTINUED

FRAME CLEANING

NAPA TEAK LA MER:

Teak does not require any special maintenance other than an occasional cleaning. If left to age naturally, the surface of the wood will gradually change to a soft silvery-grey as the pigments fade. We recommend that you maintain the silver patina with regular, gentle cleaning with soft-soap flakes dissolved in warm water (not detergent).

Be sure to use a non-abrasive brush or sponge when cleaning, and avoid using steel wool or wire brushes. When finished, rinse the entire piece of furniture with low-pressure water to remove any dirt or remaining solution.

Treating teak with oils or other preservatives is not necessary for protection, and will not extend the life of your furniture. However, if you prefer to keep your teak furniture at its original golden color — instead of letting it weather to a silvery-gray patina — use a high quality teak wood protector or conditioner.

For stained or dirty teak, use a cleaner specifically designed for Teak wood.

A recommendation is Frontgate’s Teak Cleaner and Teak Protector, however, other brands may be used.

http://www.frontgate.com/text/content/moreinfo/teak.html#cleaning

NAPA LA MER – POLYETHALENE FRAME:

This high density Polyethalene Frame is easy to clean with soap and water, and brush. For a deep cleaning, use a 10 to 1 water/bleach solution. After cleaning, rinse with fresh water.

HYDRAULIC LEGS

The stainless steel legs should be cleaned and lubricated often. Clean with a petroleum based lubricant such as WD-40. Lubricate with lithium grease. This will help to maintain smooth raising and lowering of your table. This should be done at least every 3 months and more often if table is used often. To clean, raise the table to its highest height position. Spray WD-40 onto clean, then, with a lint-free cloth, wipe the legs from top to bottom several times. Check to see if any foreign material is stuck on surface. (WD-40 applied thick and left a minute will help loosen most common materials. Wipe clean.) To lubricate, raise table to its highest position. Lubricate well on the exposed leg and raise and lower the table 2-3 times to distribute the lubricant. Wipe off excess at leg bottom.

DO NOT USE soap and water for cleaning the legs.

DRAINING YOUR TABLE CUSHIONS

It is recommended that you place the removable cushions from your table in a place where they can breath on a daily basis. Simply remove them from the table and rest them on their sides.

Section 3 - Continued

## MAINTENANCE

- It is recommended that at the same time you lubricate the leg shafts, you should also check the leveling feet to be sure the table is level and stable.

The “level or balance” of your table is very important, both during the initial set up and on a routine basis. The balance of the table is adjusted with the leveling feet, located on the bottom of each leg. You will need (2) open end wrenches – ½” and 9/16”.

Begin by taking a visual inspection of the flat bottom foot of each leg. Notice two hex nuts on each leveling foot. The upper hex nut is adjustable and secures the leveling foot in place, while the lower nut is stationary, and allows you to raise and lower each leveling foot independent of each other. This is necessary as floors and carpet may not be 100% level or flat. The most common symptom of an unbalanced table is unusual rocking of the entire bed. To determine which foot to adjust, attempt to “rock” your table. If your table rocks, the leg that is “off the ground” is the one that will need adjusting. Once your diagnosis has been made, proceed as follows:

- Raise table height to approximately 6 inches off the floor.

- Using a clean, lint free cloth, grab the silver extrusion (leg) to prevent it from moving during the adjustment.

- Loosen the upper hex nut until it no longer touches the upper leg.

- Raise or lower the entire foot as necessary on the lower hex nut. Counterclockwise will lower the overall height; clockwise will raise the overall height. Continue with the adjustment of the lower hex nut until the black round foot is completely flat to the ground and the table no longer rocks.

- To lock into place, reposition the upper hex nut so that is secure and tight against the upper leg.

- Test all legs to ensure that the upper hex nut is tight against the upper leg and secure in place.

#### Section 4

#### TECHNICAL SERVICE

With proper maintenance, your Living Earth Crafts table is designed to give you years of trouble free operation.  If you should have a problem with your table, do not attempt to repair the table yourself.  This will void the 2-year warranty that covers your table against defects in material and workmanship. It covers repairs only if you follow these steps:

- Call 800-358-8292

Our Customer Service Representative will ask you to provide the following information:

- your table’s serial number (located on the underside of the head

section of the table top)

- a description of the problem

- Our representative will coordinate a technician in your area if one is available.  The technician will contact you to arrange for a convenient time for on-site service. This service is scheduled during normal business hours, 8.AM to 5.PM, Monday through Friday.

- You will need to allow the technician access to your table at the scheduled time.  If there is a lengthy delay, you will be charged for the delay time at the service agent’s hourly rate.  To cancel the appointment, notify the technician 24 hours prior to the scheduled appointment.  If you fail to notify the technician, you will be charged for the service call.

- Please remember that any unauthorized service will not be covered.  Please be sure to contact us first.

- As expressed in your warranty, damage from abuse or mishandling is not covered.

#### Section 5

#### WARRANTY

Applies to All Napa Table Models

## Tables are warranted against defects in materials, design and workmanship, to the original owner, as follows:

## Frame

## - Lifetime (

## Foam & Vinyl

## - 3 years

## Hydraulic System, Controls,

## - 2 years

## Warranty is onsite where available.

## Warranty does not cover damage caused by accident, misuse, or neglect. All warranties limited to repair or replacement, at our discretion, to the original purchaser.

## ( Lifetime warranty applies to original owner, as long as you own your table or 5 years after the model is discontinued or five years for private label tables.

## Section 6

## NAPA LA MER MANUAL HYDRAULIC LIFT

## SPECIFICATIONS

FEATURES:

(Top Width options:  31”

(Length:  73”

(Premium Marine Grade Foam – 2.5 inches

( Napa Teak La Mer: treated Teak Wood

(Napa La Mer: High Density Polyethalene Frame

(Height Range: 25” to 37” (standard)

(Manual Hydraulic Lift – Fold Away Crank

(Lifting capacity:  500 lbs

(Standard Base: Slotted Shelf on Napa Teak La Mer

(Standard Base: Trestle on Napa La Mer

TECHNICAL DATA – HYDRAULIC LIFT SYSTEM

(Hydraulic system:  Suspa